## Slide 1
SmartGarden
A garden that measures, decides and waters itself.
Three plants on a kitchen windowsill today. Dozens of beds across a garden later — without a rewrite in between.
Phase 1 blueprint · Rev A · September 2026 · Slav Petkovic
Notes: SmartGarden is a sensor-driven irrigation and lighting system running on a Raspberry Pi 5. This deck covers what it does, how it is used, and where it goes next.

## Slide 2
THE PROBLEM
Growing things is a data problem solved by guesswork
01
Schedules ignore reality
Watering every Sunday takes no account of heat, humidity or how much light a plant actually received that week.
02
The signal exists — nobody reads it
Soil moisture, light and vapour pressure deficit are cheap to measure. Almost no one measures them, so care stays a guess.
03
Failure is silent
A plant under stress looks fine for days, then doesn't. By the time the symptom is visible the damage is already done.
Notes: Frame: this is not a gadget looking for a use. Care decisions are made on schedules and intuition when the underlying signals are cheap to measure.

## Slide 3
THE SYSTEM
A closed loop that runs entirely on your own hardware
A Raspberry Pi 5 reads air, light and soil every few seconds, stores every measurement, decides when to water and when to supplement light, and does it — logging the reason for every decision it makes. No cloud service, no subscription, no account.
3
sensor types
air · light · soil
10s
measurement tick
60s for soil
100%
local
no cloud dependency
72
requirements
specified before code
What it measures
BME680
Air temperature · humidity
pressure · gas resistance
VEML7700
Ambient light in lux, with gain
and integration time recorded
Adafruit Seesaw
Soil capacitance
and soil temperature
Notes: Everything runs on-device. Vapour pressure deficit is derived from temperature and humidity on every tick and stored as a first-class channel.

## Slide 4
HOW IT WORKS
Sense, store, decide, act — and write down why
SENSE
Drivers poll the I2C bus on their own schedules. A failed read is retried and recorded, never silently dropped.
›
STORE
Every reading lands in a local SQLite database as one narrow row. Raw for a week, minute data for 90 days, quarter-hour forever.
›
DECIDE
Rules compare each plant against its own targets: a moisture band with hysteresis, and a daily light integral goal.
›
ACT
Valves and grow lights are switched — then the result is measured, so cause and effect are recorded as a pair.
Two processes, one database
The control loop and the web dashboard are independent services that share only the database. The dashboard can crash, be redeployed or be switched off entirely and the watering never stops. A "water now" tap from a phone becomes a queued command the loop picks up on its next tick.
Notes: The key architectural decision: SQLite is the message bus. Neither process imports the other. Manual actions pass through the same safety guards as automatic ones.

## Slide 5
IN DAILY USE
Everything you need is on one phone screen
Today
Monstera
Moisture 62% · OK
Basil
Moisture 28% · Watering
Fern
Light 4.1 / 6.0 DLI
Installed as an app · works offline
1
Is anything thirsty?
Plant cards show current moisture and light against each plant's own target — at a glance, from anywhere.
2
What actually happened?
History charts mark every watering on the time axis, so you can see the moisture response it produced.
3
Why did it do that?
A plain-language decision log records the inputs the system saw and the reason for the action it chose.
4
Take over any time
Water or light a zone manually, retune thresholds from your phone, or pause all automation — no restart, no SSH.
Notes: The interface is a JSON API first; the phone app is its first consumer. Recent readings stay visible when the network drops, marked with their age rather than presented as current.

## Slide 6
TRUST
Three independent brakes on every actuation
LAYER 1
Configured limits
Watering windows, a daily water budget per zone and an hourly pulse cap. A guard can veto an action or shorten it — never lengthen or create one.
LAYER 2
Driver-enforced maximum
Every device declares its own maximum on-time, enforced inside the driver regardless of what the caller asks for.
LAYER 3
Independent watchdog
A separate thread tracks on-time per device and forces anything overdue off — and a standalone shutdown script drives every output safe even if the application itself is gone.
Guards only ever subtract. Two of the three layers reach the hardware without the control loop participating — which is precisely the condition in which a valve gets stuck open.
Notes: This is the slide that answers 'what if it breaks'. Safety is enforced at three levels that fail independently, and is verified by test.

## Slide 7
WHY IT SCALES
Three plants and three hundred are the same system
TODAY
One windowsill
Three plants, one Raspberry Pi, sensors on a single I2C bus, simulated valves until the irrigation hardware arrives.
›
LATER
Dozens of beds
Battery-powered nodes out in the garden posting readings to the same ingest endpoint — indistinguishable downstream from a local sensor.
Measurements are channels, not columns
Adding a sensor type is one driver file and one config line. Storage, API and interface change not at all.
Rules bind to roles, not to devices
A rule targets "soil moisture in zone 2". Swap the sensor or move it to another multiplexer channel and every rule still holds.
Remote nodes are already first-class
The ingest API and per-node staleness tracking ship in Phase 1; only the hardware is outstanding.
Notes: This is the primary design constraint of the whole build: adding a sensor must not touch storage, API or UI code.

## Slide 8
WHAT COMES NEXT
Each phase earns the next one's data
PHASE 1
Now
Real sensors, simulated valves
Threshold watering with hysteresis
Lighting to a daily light integral
Phone dashboard and decision log
Three-layer safety and alerting
PHASE 2
Once data exists
Forecasting how fast soil dries — time-to-stress rather than a straight line
Dose calculated from a learned absorption model, not a fixed pulse
Wireless nodes in outdoor beds
Weather forecast as another input
PHASE 3
Later
Native mobile app on the same JSON API
Plant imagery and visual health tracking
Season-over-season comparison
Multi-garden / multi-site
No model is fitted until several weeks of varied data exist. Phase 1 is built so that data comes out in the right shape — vapour pressure deficit stored on every tick, and every watering recorded with its before and after state.
Notes: The Phase 2 target is chosen and singular: moisture decay forecasting. Everything in Phase 1's data model exists to make that possible later, because it cannot be backfilled.

## Slide 9
WHERE IT STANDS
Specified in full. Built in six reviewed layers.
01
Foundation
02
Storage
03
Drivers
04
Runtime
05
API
06
Interface
Layers 1–3 run on a laptop with no hardware at all. Layer 4 is the first that needs the Pi.
The immediate next step is not more code.
After the driver layer, the sensors run for several days with automation switched off, so that real watering thresholds come from what the soil actually reports — not from a number carried over from the old system.
SmartGarden · Phase 1 · Rev A · September 2026
Notes: Close on the discipline point: the calibration step before automation is what separates a system that works from one that merely runs.